## Slide 1: Sensor and Sensing Technology
Presenting to
Professor Zhang, Yikui
School Computer Software
Presenting by
MOHAMMED ALGAMALI 6118000082
Taiabur Rahman 6218000126
Mansoor Saleh 6218000158

## Slide 2: third eye Smart shoes for Blind MAN

## Slide 3: Real-life effect
This project is intended to be developed as tool or aid that will help blind man in moving, by mean facilitates the life of the blind man.
The dependency on others is reduced and these people can become more self-reliant.
Can be used by people with poor eyesight.
Image source: internet

## Slide 4: Third eye project feature
Directions Guide
Speech Guide (Alert) simulate with software interface
Sound buzzer (Alert)
Remote Tracking (Extension)
Image source: internet

## Slide 5: Require Component
Arduino Nano Board
Ultrasonic Sensor
Acceleration Sensor
Headphone/buzzer
Vibration motor
Image source: internet

## Slide 6: How to work it
Object
Sensor
Input
Output
Processing
Arduino Nano
Sound & vibration
Image source: internet

## Slide 7: Arduino nano Board
Image source: internet
Arduino Nano Front
Arduino Nano

## Slide 8: Arduino nano Board
Image source: internet
Specifications:
Microcontroller : Atmel ATmega168 or ATmega328
Operating Voltage : 5 V
Input Voltage : 7-12 V
Digital I/O Pins :14 (of which 6 provide PWM output)
Analog Input Pins : 8
DC Current per I/O Pin : 40 mA
Flash Memory : 16 KB
Clock Speed : 16 MHz

## Slide 9: Ultrasonic Sensor
Image source: internet
Specifications:
Ultrasonic Ranging Module HC - SR04
Operating Voltage : 5 V
Accuracy : 3mm
Measuring angle covered : <15°
Operating Current : <15mA
Operating Frequency : 40Hz

## Slide 10: Ultrasonic Sensor
Image source: internet
Pin Configuration:
VCC: The Vcc pin powers the sensor, typically with +5V
Tigger: Trigger pin is an Input pin. This pin has to be kept high for 10us to initialize measurement by sending US wave.
Echo: Echo pin is an Output pin. This pin goes high for a period of time which will be equal to the time taken for the US wave to return back to the sensor.
Ground: This pin is connected to the Ground of the system

## Slide 11: Ultrasonic Sensor
Image source: internet
Arduino Nano Pin | Ultrasonic Sensor Pin
5v | VCC
GND | GND
I/O pin | GND
I/O pin | ECHO

## Slide 12: Accelerometer Sensor
Image source: internet
Digital Output: I2C
Operating Voltage : 5V/3.3V
Low Power Consumption
Faster load the appropriate speed
Ideal for noisy power environment
Pin Standard 100mil (2.54mm)

## Slide 13: Vibrating Disk Motor
Image source: internet
Motor construction : 10- Flat coreless vibration motor
Coil construction : Flat coreless core
Rated Load : Vibration weight
Rotation direction : CCW or CW
Motor position: Any position available
Voltage range for use: DC 2.5V - 3.5V
Allowable temperature range: -20ºC to 70ºC

## Slide 14
Project Software (interface)
Image source: internet

## Slide 15: Mac and Windows Interface
Using software to control the hardware device ,the speech guide and power button will be simulated with this Mac & Win application interface.
Mac interface program: Xamarin Cocoa C# & Xcode.
Windows interface program: Visual studio c#.
Image source: internet

## Slide 16: What has been done!?:
All the sensors that we got, were successfully tested.
Program Arduino with visual C# in PC and Xamarin C# were successfully tested.
Image source: internet

## Slide 17: Connect Arduino with Mac c# programing
using System.IO.Ports;
myPort = new SerialPort();
myPort.BaudRate = 9600; myPort.PortName = "/dev/cu.wchusbserial1410"; myPort.Open();
Image source: internet

## Slide 18: Connect Arduino with windows c# program
using System.IO.Ports;
myPort = new SerialPort();
myPort.BaudRate = 9600; myPort.PortName = COM4"; myPort.Open();
Image source: internet

## Slide 19: Testing c# program communicate with Arduino
Image source: internet

## Slide 20: Testing c# program communicate with Arduino (Video)
Image source: internet

## Slide 21: Arduino Code for the Project
Image source: internet

## Slide 22: C# Programming interface for the Project
Image source: internet

## Slide 23: Testing c# program communicate with Arduino (Video)
Image source: internet

## Slide 24
Project Mobile App
Image source: internet

## Slide 25: Third eye project App feature
Speech(Sound) Alarms instead of buzzer
Sound and Vibration for 5 seconds ( Alarms)
Connected to Bluetooth (Speech- notification)
Disconnected from Bluetooth (Speech- notification)
Image source: internet

## Slide 26: Third eye project icon
Image source: internet

## Slide 27: Third eye project App interface
Image source: internet

## Slide 28: Third eye project Arduino programming
Image source: internet

## Slide 29: Appinventor programming-design interface
Image source: internet

## Slide 30: Third eye project Appinventor programming
Image source: internet

## Slide 31: Appinventor programming-blocks
Image source: internet

## Slide 32: Appinventor programming-blocks
Image source: internet

## Slide 33: FAQ
Image source: internet

## Slide 34: Suggestion Box
Image source: internet

## Slide 35: Thank you